## Slide 1: Edge Detection
EN605.617.FA – Introduction to GPU Programming
Miles Gapcynski
12/10/2018

## Slide 2: Project Overview
Wanted to explore Image Processing
  Deep and interesting field
  Images can be broken down into blocks of data
Chose Edge Detection to focus scope of project
Edge Detection is a deep topic as well
  Needed specific algorithm
  Chose convolution of image data with image kernels
What can I measure and analyze?
  Compare CPU and GPU runtimes
  Analyze image data produced by different image kernels
Notes: Two motivations for choosing Image Processing
  Fascinated by image manipulation and signal processing techniques
  Algorithms can be written in SIMD fashion
Edge Detection can be used in object and pattern recognition applications, as well as photo editing software
  Didn’t want to explore machine learning (another deep topic)
  Image kernel also known as convolution matrix, mask, or filter
Edge Detection produces images with highlighted edges
  Can compare how long it takes to produce the imagery
  Can analyze different kernel outputs to determine how they might be used in different scenarios

## Slide 3: Implementation - Convolution and Kernels
Convolution is a common approach for filtering image data
  Multiply pixel and neighbors with image kernel
  Perform summation of multiplication results
  Perform these steps on every pixel
Kernels represent weights that filter image data
Gradient operators (kernels) exist that specialize in finding edges
  Two different matrices for finding horizontal or vertical edge
  Calculate magnitude of convolution results for edge intensity
Notes: Multiply pixel and neighbors with corresponding positions in kernel
Kernel applied to each pixel in an iterative fashion
  Slides over each row and column one by one
Must deal with neighbors outside of edge boundaries
  Ignore outermost rows/columns
  Perform techniques such as zero padding, replicating, or wrapping

## Slide 4: Implementation - Convolution and Kernels (cont.)
Figure 1 – Convolution (Kazemi, Figure 3)

## Slide 5: Implementation - Convolution and Kernels (cont.)
Chose three image kernels to compare: Prewitt, Roberts, and Sobel
Notes: Prewitt operator “is more sensitive to vertical and horizontal edges than diagonal edges” (Crane, 86)
Roberts operator “has a smaller effective area than other masks, making it more susceptible to noise. The other masks are better able to average out fluctuations” (Crane, 86)
Sobel operator “is more sensitive to diagonal edges than vertical and horizontal edges” (Crane, 86)

## Slide 6: Implementation - General Approach
Structure of file formats varies
  1 to N channels of values per pixel represented by different bit depths
  Channel values can be interleaved or sequential
Decided to use FreeImage library
  Open-source library specializing in read/writing image files
  Wrote utility methods to interface with library
Focused on how to convolve grayscale vs color images
  Iterate over grayscale data and convolve with image kernels
  Converted color images to grayscale
Notes: Utility methods focused on reading/writing image files, and mapping image data into channel-separated RGB values
  All red channel values, then all green, then all blue
  I found this easier to index into array for each pixel and neighbors
Converted color image data to grayscale
  Didn’t need to retain the color information (edges still present in grayscale)
  Average the RGB channel values to convert to grayscale

## Slide 7: Implementation - General Approach (cont.)
Figure 2 – Test Image and Grayscale

## Slide 8: Implementation - CPU Approach
Nested for loop iterates over rows and columns of image data
  Skipped outermost rows/columns to avoid boundary issues
  Apply gradient operator to each pixel and surround neighbors
  Calculate magnitude of row and column convolution results
Repeat for all three gradient operators

## Slide 9: Implementation - GPU Approach
Copy image and filter data to GPU
Decompose image data into grid of blocks
  Created 2D grid made up of 16x16 blocks
Execute kernel
  Utilized same filter method as CPU
  Created global and shared memory kernels for additional comparison
Copy image data back to host
Repeat for all three gradient operators, and global/shared memory kernels

## Slide 10: Implementation - HSV
Found other color models during research
  Color models provide different view of image data
Chose to implement Hue, Saturation, and Value (HSV) color model
  Hue indicates how similar a color is to red, green, or blue
  Saturation refers to intensity/purity of a color
  Value represents the maximum value of the RGB components
Could now compare three image kernels across multiple color models

## Slide 11: Implementation - HSV (cont.)
Figure 3 – Test Image (TL), Hue (TR), Saturation (BL), and Value (BR)

## Slide 12: Analysis - Grayscale vs HSV (Prewitt)
Figure 4 – Grayscale (TL), Hue (TR), Saturation (BL), and Value (BR)
Grayscale and Value output highlight less distinct edges
  Ex. Feathers
Hue output seems to focus on just the birds
  Could be useful for object recognition algorithms
Saturation output has concentrated intensity around the eyes and beaks
  Could be useful for facial recognition algorithms
Notes: “More sensitive to vertical and horizontal edges than diagonal edges” (Crane, 86)

## Slide 13: Analysis - Grayscale vs HSV (Roberts)
Figure 5 – Grayscale (TL), Hue (TR), Saturation (BL), and Value (BR)
Grayscale and HSV comparisons match those made in the Prewitt section
Comparison to Prewitt output
  Seems to do a better job at highlighting just the birds in the image
  Appears to be less noisy
Notes: “More sensitive to vertical and horizontal edges than diagonal edges” (Crane, 86)

## Slide 14: Analysis - Grayscale vs HSV (Sobel)
Figure 6 – Grayscale (TL), Hue (TR), Saturation (BL), and Value (BR)
Grayscale and HSV comparisons match those made in the Prewitt section
Comparison to Prewitt and Roberts output
  Output quite similar to Prewitt output
  A bit noisier than other two gradient operators
  Seems to do a better job at finding the diagonal edges in the image
Notes: “More sensitive to vertical and horizontal edges than diagonal edges” (Crane, 86)

## Slide 15: Analysis - Timing Results
Image | Image Dimensions (total pixels) | CPU Execution Times (ms) | GPU Execution Times (ms) | 
 |  |  | Global Memory | Shared Memory
mountains.jpg | 500 x 348 (174,000) | 10.6232 | 0.5930 | 0.6353
lena.png | 512 x 512 (262,144) | 16.0494 | 0.7689 | 0.9739
birds.jpg | 700 x 533 (373,100) | 24.1710 | 1.1357 | 1.1654
church.jpg | 1024 x 768 (786,432) | 48.7879 | 1.9197 | 2.2372
pisa.jpg | 1600 x 900 (1,440,000) | 88.7504 | 3.5310 | 3.7038
valley.jpg | 2560 x 1440 (3,686,400) | 228.5247 | 7.8206 | 8.3551
town.jpg | 3840 x 2160 (8,294,400) | 516.8103 | 17.3303 | 18.7000
Figure 7 – Timing Results

## Slide 16: Analysis - Timing Results (cont.)
Figure 8 – Timing Results

## Slide 17: Conclusion
GPU considerably better than CPU processing image data in SIMD fashion
  Discrepancy grows substantially as image data size increases
  CPU would have better results with multithreading support
Global memory kernel outperformed shared memory kernel
  Surprising, though difference is quite small
Pros and cons of each gradient operator made evident by RGB/grayscale and HSV color model output
Possible project extensions and improvements
  Implement additional edge detection algorithms, gradient operators, and color models
  Utilize pixel thresholds to reduce noise in output
  Analyze filtered image data further using object/pattern recognition algorithms
  Utilize texture memory, NPP library, and/or different block sizes for potential GPU improvements

## Slide 18: Works Cited
Crane, Randy. A Simplified Approach to Image Processing: Classical and Modern Techniques in C. Prentice Hall PTR, 1997.
Kazemi, Hadi. “Image Filtering.” Machine Learning Guru, 6 Feb. 2017, 15:52:07, machinelearninguru.com/computer_vision/basics/convolution/image_convolution_1.html.