## Slide 1: Edge Detection on the CPU and GPU
EN605.617.FA – Introduction to GPU Programming
Miles Gapcynski
12/10/2018

## Slide 2: Agenda
Project Overview
Implementation
  Convolution and Kernels
  General Approach
  CPU and GPU Approach
  HSV
Analysis
  Grayscale vs HSV
  Timing Results
Conclusion

## Slide 3: Project Overview
Wanted to explore Image Processing
  Deep and interesting field
  Images can be broken down into blocks of data
  Chose topic of Edge Detection to focus scope of project
What is Edge Detection?
  Edge Detection produces image data that highlights edges in a picture
  Useful for computer vision, object recognition, and photo editing software
How to perform Edge Detection?
  Utilize convolution algorithm to filter image data in search of edges
What can I measure and analyze?
  Compare CPU and GPU runtimes
  Analyze image data produced by different filters (kernels)

## Slide 4: Implementation - Convolution and Kernels
Convolution is a common approach for filtering image data
  Multiply pixel and neighbors with kernel values
  Perform summation of multiplication results
  Perform multiplication and summation for every pixel
Kernels represent weights that filter image data
  Also known as convolution matrices, masks, or filters

## Slide 5: Implementation - Convolution and Kernels (cont.)
Figure 1 – Convolution (Kazemi, Figure 3)

## Slide 6: Implementation - Convolution and Kernels (cont.)
Chose three gradient operators to compare: Prewitt, Roberts, and Sobel
  Two specialized kernels for finding horizontal or vertical edges
  Calculate magnitude of convolution results for edge intensity

## Slide 7: Implementation - General Approach
Structure of file formats varies
  Different file header structures
  1 to N channels of values per pixel represented by different bit depths
Decided to use FreeImage library
  Open-source library specializing in read/writing image files
  Wrote utility methods to interface with library
Focused on how to convolve grayscale vs color images
  Iterate over grayscale data and convolve with image kernels
  Converted color images to grayscale

## Slide 8: Implementation - General Approach (cont.)
Figure 2 – Test Image and Grayscale

## Slide 9: Implementation - CPU Approach
Nested for loop iterates over rows and columns of image data
  Skipped outermost rows/columns to avoid boundary issues
  Apply gradient operator to each pixel and it’s neighbors
  Calculate magnitude of row and column convolution results
Repeat for all three gradient operators

## Slide 10: Implementation - GPU Approach
Copy image and gradient operators to GPU
Decompose image data into grid of blocks
  Created 2D grid made up of 16x16 blocks
Execute kernel
  Utilized same convolution method as CPU
  Created global and shared memory kernels for additional comparison
Copy image data back to host
Repeat for all three gradient operators, and global/shared memory kernels

## Slide 11: Implementation - HSV
Found other color models during research
  Color data represented in ways besides RGB model
Chose to implement Hue, Saturation, and Value (HSV) color model
  Hue indicates how similar a color is to red, green, or blue
  Saturation refers to intensity/purity of a color
  Value represents the maximum value of the RGB components
Could now compare three image kernels across multiple color models

## Slide 12: Implementation - HSV (cont.)
Figure 3 – Test Image (TL), Hue (TR), Saturation (BL), and Value (BR)

## Slide 13: Analysis - Grayscale vs HSV (Prewitt)
Figure 4 – Grayscale (TL), Hue (TR), Saturation (BL), and Value (BR)
Grayscale and Value output highlight less distinct edges
  Ex. Feathers
Hue output seems to focus on just the birds
  Could be useful for object recognition algorithms
Saturation output has concentrated intensity around the eyes and beaks
  Could be useful for facial recognition algorithms

## Slide 14: Analysis - Grayscale vs HSV (Roberts)
Figure 5 – Grayscale (TL), Hue (TR), Saturation (BL), and Value (BR)
Grayscale and HSV comparisons match those made in the Prewitt section
Comparison to Prewitt output
  Seems to do a better job at highlighting just the birds in the image
  Appears to be less noisy, but features are less distinguishable (dark)

## Slide 15: Analysis - Grayscale vs HSV (Sobel)
Figure 6 – Grayscale (TL), Hue (TR), Saturation (BL), and Value (BR)
Grayscale and HSV comparisons match those made in the Prewitt section
Comparison to Prewitt and Roberts output
  Seems to do a better job at finding the diagonal edges in the image
  Noisier than Prewitt and Roberts

## Slide 16: Analysis - Timing Results
Image | Image Dimensions (total pixels) | CPU Execution Times (ms) | GPU Execution Times (ms) | 
 |  |  | Global Memory | Shared Memory
mountains.jpg | 500 x 348 (174,000) | 6.3000 | 0.4530 | 0.4285
lena.png | 512 x 512 (262,144) | 9.6186 | 0.5202 | 0.4687
birds.jpg | 700 x 533 (373,100) | 15.9758 | 0.6813 | 0.5651
church.jpg | 1024 x 768 (786,432) | 28.9552 | 1.0745 | 0.8162
pisa.jpg | 1600 x 900 (1,440,000) | 52.4860 | 1.5420 | 1.2809
valley.jpg | 2560 x 1440 (3,686,400) | 135.4677 | 3.0519 | 2.0822
town.jpg | 3840 x 2160 (8,294,400) | 306.9337 | 7.9471 | 5.11236
Figure 7 – Timing Results

## Slide 17: Analysis - Timing Results (cont.)
Figure 8 – Timing Results

## Slide 18: Conclusion
GPU considerably faster than CPU at processing image data
  Discrepancy grows substantially as image data size increases
  CPU would have better results with multithreading support
Shared memory kernel outperformed global memory kernel
Pros and cons of each gradient operator made evident by RGB/grayscale and HSV color model output
Possible project extensions and improvements
  Implement additional edge detection algorithms, gradient operators, and color models
  Utilize pixel thresholds to reduce noise in output
  Analyze filtered image data further using object/pattern recognition algorithms
  Utilize texture memory, NPP library, and/or different block sizes for potential GPU improvements

## Slide 19: Works Cited
Crane, Randy. A Simplified Approach to Image Processing: Classical and Modern Techniques in C. Prentice Hall PTR, 1997.
Kazemi, Hadi. “Image Filtering.” Machine Learning Guru, 6 Feb. 2017, 15:52:07, machinelearninguru.com/computer_vision/basics/convolution/image_convolution_1.html.